## Slide 1: Lesson 4
Computer Networking

## Slide 2: Topic Objectives
To know about uses, applications, disadvantages of network
To elaborate various types of network
To elaborate various types of topologies

## Slide 3: Networking
Computer network A collection of computing devices that are connected in various ways in order to communicate and share resources
Usually, the connections between computers in a network are made using physical wires or cables
  However, some connections are wireless, using radio waves or infrared signals

## Slide 4: Networking History
1961: Kleinrock - queuing theory shows effectiveness of packet-switching
1964: Baran - packet-switching in military applications for survivable networks
1967: ARPAnet conceived by Advanced Research Projects Agency
1969: First ARPAnet node operational
  Prof.Kleinrock sends a message across from UCLA to Stanford
1972:
  ARPAnet demonstrated publicly
  NCP (Network Control Protocol) first host-host protocol
  First e-mail program
  ARPAnet has 15 nodes

## Slide 5: Networking History
1970: ALOHAnet satellite network in Hawaii (CSMA developed), later connects to ARPANet
1973: Bob Metcalfe’s PhD thesis proposes Ethernet (CSMA/CD developed)
1974: Cerf and Kahn - architecture for interconnecting networks: the word “Internet” makes its appearance from Cerf’s writings

## Slide 6: Networking History
Early 1990’s: ARPAnet decommissioned
Early 1990s: WWW
  Hypertext (1945 Bush: “As We May Think” article, Ted Nelson, Engelbert, Andries in 1968 )
  HTTP: Tim Berners-Lee develops WWW an Internet based hypermedia initiative at CERN, specifies URLs, HTTP and HTML which became basis for today’s WWW
  1994: Mosaic (Univ. of Illinois), later Netscape the major browsers until late 1990’s
  late 1990’s: commercialization of the WWW, with introduction of HTTPS e-commerce is realized
Late 1990’s:
est. 50 million computers on Internet
est. 100 million+ users
backbone links running at 1 Gbps

## Slide 7: Networking
The generic term node or host refers to any device on a network
Data transfer rate The speed with which data is moved from one place on a network to another
Data transfer rate is a key issue in computer networks

## Slide 8: Networking
Computer networks have opened up an entire frontier in the world of computing called the client/server model
Client/Server interaction

## Slide 9: Networking
File server A computer that stores and manages files for multiple users on a network
Web server A computer dedicated to responding to requests (from the browser client) for web pages

## Slide 10: Types of Network
Local-area network (LAN) A network that connects a relatively small number of machines in a relatively close geographical area

## Slide 11: Types of Networks
Various configurations, called topologies, have been used to administer LANs
  Ring topology A configuration that connects all nodes in a closed loop on which messages travel in one direction
  Star topology A configuration that centers around one node to which all others are connected and through which all messages are sent
  Bus topology All nodes are connected to a single communication line that carries messages in both directions

## Slide 12: Types of Networks
A bus technology called Ethernet has become the industry standard for local-area networks
Various network topologies

## Slide 13: Types of Networks
Wide-area network (WAN) A network that connects two or more local-area networks over a potentially large geographic distance
  Often one particular node on a LAN is set up to serve as a gateway to handle all communication going between that LAN and other networks
Communication between networks is called internetworking
  The Internet, as we know it today, is essentially the ultimate wide-area network, spanning the entire globe

## Slide 14: Types of Networks
Metropolitan-area network (MAN) The communication infrastructures that have been developed in and around large cities

## Slide 15: So, who owns the Internet?
Well, nobody does. No single person or company owns the Internet or even controls it entirely. As a wide-area network, it is made up of many smaller networks. These smaller networks are often owned and managed by a person or organization. The Internet, then, is really defined by how connections can be made between these networks.

## Slide 16: Types of Networks
Local-area networks connected across a distance to create a wide-area network

## Slide 17: Internet Connections
Internet backbone A set of high-speed networks that carry Internet traffic
These networks are provided by companies such as AT&T, GTE, and IBM
Internet service provider (ISP) A company that provides other companies or individuals with access to the Internet

## Slide 18: Internet Connections
There are various technologies available that you can use to connect a home computer to the Internet
  A phone modem converts computer data into an analog audio signal for transfer over a telephone line, and then a modem at the destination converts it back again into data
  A digital subscriber line (DSL) uses regular copper phone lines to transfer digital data to and from the phone company’s central office
  A cable modem uses the same line that your cable TV signals come in on to transfer the data back and forth

## Slide 19: Internet Connections
Broadband A connection in which transfer speeds are faster than 128 bits per second
  DSL connections and cable modems are broadband connections
  The speed for downloads (getting data from the Internet to your home computer) may not be the same as uploads (sending data from your home computer to the Internet)

## Slide 20: Packet Switching
To improve the efficiency of transferring information over a shared communication line, messages are divided into fixed-sized, numbered packets
Network devices called routers are used to direct packets between networks
Messages sent by packet switching

## Slide 21: Open Systems
Proprietary system A system that uses technologies kept private by a particular commercial vendor
  One system couldn’t communicate with another, leading to the need for
Interoperability The ability of software and hardware on multiple machines and from multiple commercial vendors to communicate
  Leading to
Open systems Systems based on a common model of network architecture and a suite of protocols used in its implementation

## Slide 22: Open Systems
The International Organization for Standardization (ISO) established the Open Systems Interconnection (OSI) Reference Model
Each layer deals with a particular aspect of network communication
The layers of the OSI Reference Model

## Slide 23: Network Protocols
Network protocols are layered such that each one relies on the protocols that underlie it
Sometimes referred to as a protocol stack
Layering of key network protocols

## Slide 24: TCP/IP
TCP stands for Transmission Control Protocol
  TCP software breaks messages into packets, hands them off to the IP software for delivery, and then orders and reassembles the packets at their destination
IP stands for Internet Protocol
  IP software deals with the routing of packets through the maze of interconnected networks to their final destination

## Slide 25: TCP/IP (cont.)
UDP stands for User Datagram Protocol
  It is an alternative to TCP
  The main difference is that TCP is highly reliable, at the cost of decreased performance, while UDP is less reliable, but generally faster

## Slide 26: High-Level Protocols
Other protocols build on the foundation established by the TCP/IP protocol suite
  Simple Mail Transfer Protocol (SMTP)
  File Transfer Protocol (FTP)
  Telnet
  Hyper Text Transfer Protocol (http)

## Slide 27: MIME Types
Related to the idea of network protocols and standardization is the concept of a file’s MIME type
  MIME stands for Multipurpose Internet Mail Extension
  Based on a document’s MIME type, an application program can decide how to deal with the data it is given

## Slide 28: MIME Types
Some protocols and the ports they use

## Slide 29: Firewalls
Firewall A machine and its software that serve as a special gateway to a network, protecting it from inappropriate access
  Filters the network traffic that comes in, checking the validity of the messages as much as possible and perhaps denying some messages altogether
  Enforces an organization’s access control policy

## Slide 30: Firewalls
A firewall protecting a LAN

## Slide 31: Network Addresses
Hostname A unique identification that specifies a particular computer on the Internet
For example
  matisse.csc.villanova.edu
  condor.develocorp.com

## Slide 32: Network Addresses
Network software translates a hostname into its corresponding IP address
For example
  205.39.145.18

## Slide 33: Network Addresses
An IP address can be split into
  network address, which specifies a specific network
  host number, which specifies a particular machine in that network
An IP address is stored in four bytes

## Slide 34: Domain Name System
A hostname consists of the computer name followed by the domain name
csc.villanova.edu is the domain name
  A domain name is separated into two or more sections that specify the organization, and possibly a subset of an organization, of which the computer is a part
  Two organizations can have a computer named the same thing because the domain name makes it clear which one is being referred to

## Slide 35: Domain Name System
The very last section of the domain is called its top-level domain (TLD) name
Top-level domains, including some relatively new ones

## Slide 36: Domain Name System
Organizations based in countries other than the United States use a top-level domain that corresponds to their two-letter country codes
Some of the top-level domain names based on country codes

## Slide 37: Domain Name System
The domain name system (DNS) is chiefly used to translate hostnames into numeric IP addresses
  DNS is an example of a distributed database
  If that server can resolve the hostname, it does so
  If not, that server asks another domain name server